Практическо упражнение № 4

ЗАПОЗНАВАНЕ И РАБОТА С МОДУЛ АНАЛОГОВО-ЦИФРОВ ПРЕОБРАЗУВАТЕЛ НА PIC18F452

Забележка: PSPIF, PSPIE и PSPIP са резервирани за схеми PIC18F2x2 и трябва винаги да се подържат нулирани.

IV. Задачи за изпълнение

- Да се разучат схемата и стъпките, които трябва да се изпълня-ват за конфигурирането на модула.

- Да се пресметне минималното време за следене при следните допускания: CHOLD = 120pF; RS = 10kΩ; грешка на преобразуване ≤1/2 стъпка; при VDD =5V → RSS = 7 kΩ (от графиката на фиг.4); максимална температура = 500С; VHOLD = 0V в началния момент (t = 0).

- Да се въведе програмата и да се допълнят липсващите стойности на регистрите за аналогово-цифрово преобразуване при следните условия:

- получаването на резултата да става чрез прекъсване след завършване на  преобразуването;

- формата на резултата да е ляво ориентиран;

- за такт да се използва вградения RC генератор на ADC;

- конфигурирането на входовете на ADC да стане чрез комбинацията PCFG3,PCFG2, PCFG1,PCFG0 = 0100;

- за преобразуване да се използва канал AN0;

;****************************************************

;	PIC18CXX2 EXAMPLE CODE FOR PICDEM-2

;

;	TITLE: A/D Converter Demonstration

; 	FILENAME: a2d.asm

;	REVISION HISTORY:  A 5/13/00 jb   format change

;	HARDWARE: PICDEM-2 board

;	FREQUENCY: 4MHz

;

;*****************************************************

; This program is a simple implementation of the

; PIC18C452's ;A/D. One Channel is selected (AN0).

; The hardware for this ;program is the PICDEM-2 board.

; The program converts the ;potentiometer value on RA0

; and displays it as an 8 bit binary value ;on Port B.

;

; The A/D is configured as follows:

; Vref = +5V internal

; A/D Osc. = internal RC

; A/D Channel = AN0 (RA0)

LIST P=18C452

#include <P18C452.INC>	; File contains addresses for

;register and bit names

;****************************************************

; reset and interrupt vectors

org	0x00000	; Reset Vector Address

goto	Start

org	0x00008	; Interrupt Vector Address

goto	ISR		; goto Interrupt Service Routine

;****************************************************

; program code starts here

org	0x00020

Start

clrf	PORTB		; clear all bits of PORTB

clrf	TRISB		; Set PORTB as outputs

call	InitializeAD	; configure A/D module

call	SetupDelay	; delay for 15 instruction cycles

bsf	ADCON0,GO		;  Start first A/D conversion

Main	goto	Main		; do nothing loop

;****************************************************

; Service A/D interrupt

; Get value and display on LEDs

ISR

; Save context (WREG and STATUS) if required.

btfss	PIR1,ADIF		; Did A/D cause interrupt?

goto	OtherInt			; No, check other sources

movf	ADRESH,W			; Get A/D value

movwf	LATB			; Display on LEDs

bcf	PIR1,ADIF			; Reset A/D int flag

call	SetupDelay		; Delay for 15 cycles

bsf	ADCON0,GO			; Start A/D conversion

goto	EndISR			; return from ISR

OtherInt

; This would be replaced by code to check and service other interrupt sources

goto	$				; trap here, loops to self

EndISR

; Restore context if saved.

retfie				; Return, enables GIE

;***********************************************************

; InitializeAD - initializes and sets up the A/D hardware.

; Select AN0 to AN3 as analog inputs,RC clock, and read AN0.

InitializeAD

movlw	B'xxxxxxxx'	; Make RA0,RA1,RA4 analog inputs

movwf	ADCON1

movlw	B'xxxxxxxx'	; Select RC osc, AN0 selected,

movwf	ADCON0		; A/D enabled

bcf	PIR1,ADIF			; Clear A/D interrupt flag

bsf	PIE1,ADIE			; Enable A/D interrupt

bsf	INTCON,PEIE		; Enable peripheral interrupts

bsf	INTCON,GIE		; Enable Global interrupts

return

;**********************************************************

; This is used to allow the A/D time to sample the input

; (acquisition time).

;

; This routine requires 11 cycles to complete.

; The call and return add another 4 cycles.

;

; 15 cycles with Fosc=4MHz means this delay consumes 15us.

SetupDelay

movlw	.3			; Load Temp with decimal 3

movwf	TEMP

SD

decfsz	TEMP, F		; Delay loop

goto	SD

return

END

- Изчислете измерената стойност във волти и проверете стойността с волтметър.

V. Контролни въпроси.

1. Колко регистъра има модул ADC и за какво се използват те?

2. Как се установяват изводите като аналогови входове?

3. За колко време се изпълнява AD преобразуване?

4. Какви елементи включва моделът на аналоговия вход?

5. На какво условие трябва да отговаря такта на преобразуване?

6. В какъв формат се записва резултатът от преобразуването?