## Slide 1: CMOS Analog Integrated Circuits Part 2. CMOS Biasing Circuits
Technical University of Sofia
Faculty of Electronics
ECAD Laboratory
2008
Advanced level study programme in
Electronics Design and Integration Technologies
28213-IC-1-2005-1-BE-ERASMUS-PROGUC-3 2006-2322 / 001-001 SO2
Emil D. Manolov

## Slide 2: 2. CMOS Biasing Circuits
CMOS Analog Integrated Circuits
(introductory course)
Emil D. Manolov, edm@tu-sofia.bg
Department of Electronics, Technical University – Sofia

## Slide 3: Main topics of the presentation
The presentation introduces to the basic building blocks of CMOS biasing circuits:
- Current Mirrors;
- Current References;
- Voltage References.

## Slide 4: Current mirrors
This part presents the most used current mirrors:
- simple current mirror;
- cascode current mirror;
- high-swing cascode current mirror;
- Wilson current mirror;
- regulated cascode current mirror.

## Slide 5: Current mirror definition
The current mirrors are basic building block of the analog and mixed
integrated circuits.
Their output generates a replica of the input reference current, i.e.
The ratio m between both currents can be equal, higher or smaller than 1.

## Slide 6: Current mirror model
If we look at the electric function of the circuit, the ideal current mirror is a current controlled current source (CCCS).
In practice the real current mirrors are not able to accomplish the function of a CCCS exactly.

## Slide 7: Basic current mirror
Figure shows the basic current mirror with NMOS and PMOS transistors.
The input current is Iref, the output current is Iout.

## Slide 8: Basic current mirror analysis
The operation of the circuit is based on the principle of matched devices.
If two transistors operate in strong inversion and are in saturation, the expressions for the current Iref flowing through transistor Mr, and the current Iout through Mo are:
Since the bulk-source voltages of Mr and Mo are identical we can assume that the theirs threshold voltages are identical too, i.e. VTNr = VTNo . The gate-source voltages VGSr and VGSo are the same, so the ratio of the currents is given by
Finally, the products of the channel modulation effects (λr and λo) and the drain-source voltages (VDSr and VDSo) are much smaller then 1, so the above ratio can be simplified to

## Slide 9: Basic current ratio formula
Important!
The current ratio depends mainly from the horizontal layout of the transistors, i.e. the sizes of width (W) and length (L) of the corresponding channels (see the picture).

## Slide 10: Simplified current ratio formula
The values of the sizes of the MOS transistor are a result from the designer’s dimensioning and can be implemented fairly exact in the chip. This is the reason current mirror circuits to be widely used in practice.
Current mirrors usually employ the same length for all of the transistors in order to minimize errors due to the side-diffusion of the source and drain areas (LD on the figure). Then the equation for current ratio simplifies

## Slide 11: Simulation testing of current mirrors
The figure shows a test-bench for simulation of basic characteristics of NMOS current mirror. Using this circuit the transfer (Iout=f(Iref)) and the output (Iout=f(Vout)) characteristics can be obtained.

## Slide 12: Output characteristic of NMOS current mirror
Vmin is the minimum output voltage, which guarantees the operation of the transistor Mo in saturation.
The small signal output resistance rout characterizes the dependency of the output current Iout on the output voltage Vout (the slope of the Iout vs. Iref). This resistance is equal of the output resistance of the transistor Mo.
Basic parameters:
-minimum output voltage Vmin;
-small signal output resistance rout

## Slide 13: Family of output characteristics
The figure shows a family of output characteristics for different values of Iref.
The conclusions is:
The higher Iref – the higher Vmin and the smaller rout.

## Slide 14: Transfer characteristic
The figure shows the ideal (in red) and the real (in green) transfer characteristics of a current mirror. The best fitting is between Imin and Imax of the input current Iref. The limits depend on the chosen current ratio and are different for different type of mirrors. Usually these borders fix the recommended working area of the mirror.

## Slide 15: Sensitivity of the current mirror
The sensitivity of the current mirror characterizes the dependency of the output current on the DC power supply voltage, temperature, or the process variation.
For example, the sensitivity of the Iout to VDD is defined as follows:
For reliable operation of the mirror it is necessary the value of the sensitivity to be minimal.

## Slide 16: Matching accuracy
When the current ratio m is different from 1 the two transistors in the current mirror have a different W/L ratio and consequently their layouts are not identical. Then their threshold voltages are different and also parasitic resistances appear, which reduce the power supply voltage. The formulas for the current ratio becomes more complex:
Consequently, the asymmetries in the layout of the transistors cause errors in the value of the output current. Depending on the particular case, the error of the output current can reach up to 10-20 %.

## Slide 17: System of current mirrors
Figure shows a system of current mirrors, which consists of simple current mirrors with NMOS and PMOS transistors. Near to each transistor its W/L ratio is specified. The transistors M6, M7 and M8 are current sources. The transistors M2, M3, M4 are current sinks. Check the values of the currents by using the above discussed formulas.

## Slide 18: Summing up of currents
The figure demonstrate how we can summing up different currents using current mirrors.
Transistor pairs M5-M6, M5-M7 and M2-M3 are simple current mirrors.
The current through M2 is the sum of the currents through M6 and M7.

## Slide 19: Subtracting of currents
The figure demonstrate how we can subtract different currents using current mirrors.
Transistor pairs M1-M2, M3-M4 and M5-M6 are simple current mirrors.
The current through M3 is the difference between the currents through M6 and M2.

## Slide 20: Improved current mirrors
The improved current mirrors have higher output impedance than simple current mirrors. To this aim the designers add one or several supplement transistors in series with the output one. The approach increases many times the output resistance, but enlarges important the minimum output voltage Vmin. To avoid this drawback, different solutions can be applied.
In the next slides we will discuss the most popular improved current mirror circuits:
- cascode current mirror;
- high-swing cascode current mirror;
- Wilson current mirror;
- regulated cascode current mirror.

## Slide 21: Cascode current mirror
To increase the output resistance the second transistor M2, in series with M4 is connected. The output resistance is:
As a result Vmin increases from Veff up to
The figure present the cascode current mirror with NMOS.
A similar solution with PMOS is possible, also.

## Slide 22: High-swing cascode current mirror
To decrease the Vmin of the cascode current mirror a high-swing cascode current mirror is used.
This circuit keep the high output impedance of the cascode current mirror, along with decreased value of Vmin:

## Slide 23: Wilson current mirror
The presented circuits is Wilson current mirror.
The circuit uses additional series transistor (M2) and negative feedback (implemented with M1-M3 pair) to improve the output resistance and to stabilize the output current.
The drawback of the circuit is the high value of Vmin:

## Slide 24: Regulated cascode current mirror
The figure shows the regulated cascode current mirror.
The circuit uses an additional series transistor (M2) and a negative feedback (made by transistor M3) to improve the output resistance and to stabilize the output current. The Vmin of the circuit has a high value

## Slide 25: Instructions for self-study
The past presentation gives only a first sight on the current mirror circuits. After reading and understanding the presented information you have to study the material from at least one of the following textbooks:
- R. Baker, H. Li, D.Boyce. CMOS Circuit Design, Layout and Simulation, IEEE Press, New York, 2005, ISBN 0-7803-3416-7. Chapter 20, pp.427-462.
- Ph. E. Allen, D. R. Holberg, and Allen. CMOS Analog Circuit Design, Oxford University Press, Inc., 2002. ISBN 0-19-511644-5, Chapter 4.1-4.4, pp. 113-142.
- F. Maloberti. Analog design for CMOS VLSI Systems. Kluwer Academic Publishers, 2003, eBook ISBN: 0-306-47952-4, Print ISBN: 0-7923-7550-5, Chapter 4.1, pp.155-177.
The next step in the learning process is to study the examples and complete the experiments, which are presented in Guided exercise 2 and Non-guided exercise 1.
After that you can go on to the next part : Current references

## Slide 26: Current reference circuits
The current reference circuit provides a current with high precise and stability.
The ideal current reference is independent of power supply voltage, temperature and process variation.
The figure shows the graphical representation and the large signal current characteristic of an ideal current reference.

## Slide 27: The resistor as a simple current reference
The most simple current reference is the resistor.
In this case the output current Iref is equal of:
The sensitivity of the Iref to Vout is extremely high:
The temperature coefficient depends on the used technology and is equal of the temperature coefficient of the resistor:
and for this reason more complex and precise circuits are used in the practice.

## Slide 28: Improved current reference circuits
In the next slides are presented some current reference circuits, which are weakly depended on the power supply voltage:
- Threshold voltage referenced self-biasing circuits;
- Diode voltage referenced self-biasing circuits;
- Thermal voltage referenced self-biasing circuit;
- Beta multiplier referenced self-biasing circuit.

## Slide 29: Threshold voltage referenced circuit
The reference current can be found from the equation, which demonstrate the current independency of the power supply voltage VDD.
The threshold voltage has a negative temperature coefficient, which determine the negative value of the TCIref.
Figure shows the threshold voltage referenced circuit, also called bootstrap reference.

## Slide 30: Diode voltage referenced circuit
The reference current of the diode voltage referenced circuit is independent of the power supply voltage VDD.
The voltage across resistance R is equal to the voltage across the forward biased emitter-base junction of the diode-connected transistor Q. Thus, the equation for the Iref is
where φT is the thermal voltage (about 25.8 mV at 300K), Is is the saturation current of the emitter junction of the bipolar transistor Q, n is empirical coefficient between 1 and 2.
The diode voltage has a negative temperature coefficient, which together with the positive TC of the resistor R, cause the negative value of the TCIref.

## Slide 31: Thermal voltage referenced circuit - var.1
Figure shows the thermal voltage referenced circuit, where the area of the transistor Q2 is m times higher than the area of the transistor Q1. Then, we have
where φT is the thermal voltage (about 25.8 mV at 300K), n is empirical coefficient between 1 and 2.
The thermal voltage has a positive temperature coefficient, which determine the positive value of the TCIref.
Finally, we find
i.e.

## Slide 32: Thermal voltage referenced circuit - var.2
Figure shows a second variant of the thermal voltage referenced circuit, where the areas of the transistors Q1 and Q2 are equal. Then, the equation for the reference current is the same as in previous variant, but in this case m is the current ratio:

## Slide 33: Beta multiplier referenced circuit – var.1
The circuit has a positive temperature coefficient.
The beta multiplier referenced circuit has two basic operating modes.
In the first case all transistors work in strong inversion, saturation region, so we can find that

## Slide 34: Beta multiplier referenced circuit - var.2
In the second case transistors M1 and M2 work in weak inversion (sub-threshold region). As we know in this region the behavior of the MOS transistor is like to the bipolar one. The corresponding equations are:
The last equation confirm the independence of reference current of the power supply voltage. The circuit has a positive temperature coefficient. It is useful for operation in low-voltage, low-power circuits.

## Slide 35: Temperature coefficients
As it is presented in the previous slides, the temperature coefficients of the discussed circuits depend on the applied principle of stabilization of the reference current.
To compute the corresponding temperature coefficients of the consider circuits we can use the following data:
Typical values of the TCR for n=well, n+/p+ (active) and poly resistors are: 10000, 2000 and 1000[ppm/oC] respectively. (1ppm/oC=10-6/oC)
The temperature coefficient of the threshold voltage is about -3000[ppm/oC].
The temperature coefficient of the diode voltage is approximately -3300[ppm/ oC] (-2mV /oC ).
The temperature coefficient of the thermal voltage is approximately +3300[ppm/oC] (0.085mV/oC).
The temperature coefficient of the mobility µ is equal of -1.5/T[oC-1].

## Slide 36: Simulation testing of current reference
The figure shows a recommended connection for simulation of basic characteristics of current reference circuits. M6 imitates the load in this circuit.
Using the presented test-bench the dependency of the reference current vs. power supply voltage Iref=f(VDD) and the temperature characteristic Iref=f(T) can be obtained.

## Slide 37: The reference current vs. power supply voltage
Figure shows reference current vs. power supply voltage characteristic - Iref=f(VDD).
From this characteristic we can read that the minimum power supply voltage, which guarantees the circuit operation is about 1.8V.
Also, we can examine that the output resistance in operating region is higher then 2M.

## Slide 38: Temperature characteristic
Figure shows the reference current vs. temperature characteristic - Iref=f(T).
We can read that the difference between the minimal and maximal values of the reference current for the 200oC temperature range is 8.6uA. Consequently the temperature coefficient is about 43nA/oC (i.e. 0.22%/oC).

## Slide 39: Instructions for self-study
The past presentation gives only a first sight on the current references. After reading and understanding the presented information you have to study the material from at least one of the following textbooks:
- R. Baker, H. Li, D.Boyce. CMOS Circuit Design, Layout and Simulation, IEEE Press, New York, 2005, ISBN 0-7803-3416-7. Chapter 21.2 (pp.469-476) and 21.4 (480-488).
- Ph. E. Allen, D. R. Holberg, and Allen. CMOS Analog Circuit Design, Oxford University Press, Inc., 2002. ISBN 0-19-511644-5, Chapter 4.5, pp. 143-152.
- F. Maloberti. Analog design for CMOS VLSI Systems. Kluwer Academic Publishers, 2003, eBook ISBN: 0-306-47952-4, Print ISBN: 0-7923-7550-5, Chapter 4.2, pp.178-195.
The next step in the learning process is to study the examples and complete the experiments, which are presented in Guided exercise 3 and Non-guided exercise 2.
After that you can go on to the next part : Voltage references

## Slide 40: Voltage references
The last part of the presentation contains the information about basic voltage reference circuit:
- voltage dividers;
- band-gap voltage reference;
- beta multiplier voltage reference.

## Slide 41: Voltage reference definition
The voltage reference circuit provides a voltage with high precise and stability.
The ideal voltage reference is independent of power supply voltage, temperature and process variation.
The figure shows the graphical representation and the large signal current characteristic of an ideal voltage reference.

## Slide 42: Voltage dividers
The most typical voltage dividers are shown in the figure.
The left circuit is conventional voltage divider formed with two resistors. The big problem with this solution is that in order to reduce the current consumption the resistors must be too large, which increases the area of the die.
The second circuit uses NMOS transistor and resistor. The reference voltage is equal of:
and depends strongly on the power supply voltage and the absolute tolerance of the resistance R.

## Slide 43: The MOS-only voltage divider
The third circuit is most frequently used in practice. In this circuit both transistors operate in strong inversion, saturation region. The currents through M1 and M2 are equals and we can write
The formula demonstrates the strong dependency of the reference voltage Vref on the power supply voltage VDD. The circuit is characterized with high temperature and process variation instability.
Consequently, the equation for the reference voltage is given by

## Slide 44: Improved voltage reference circuits
The main drawback of using voltage dividers is that they are very sensitive to the power supply voltage and temperature.
In the next slides are presented two widely used improved voltage reference circuits, which are weakly depended on the power supply voltage and temperature:
- Band-gap voltage reference;
- Beta multiplier voltage reference.

## Slide 45: Band-gap voltage reference
Band-gap voltage reference compensates the positive TC of the thermal voltage current source with the negative TC of the diode forward voltage. In the presented circuit the area of the Q2 is m times higher than the area of the Q1. Thus
The condition for the temperature compensation is
Finally, for compensated circuit, we can find
and consequently
i.e.

## Slide 46
Band-gap voltage temperature compensation
Figure demonstrates the temperature compensation in the band-gap voltage reference. The current I, which is generated by the thermal voltage current source has positive TC (the upper chart). The voltage VE(Q3) between the emitter and the base of the diode connected transistor has a negative TC. As a result the reference voltage, which is the sum of the emitter-base voltage and the voltage drop across the resistance L.R, depends very weakly from the temperature (lower chart).

## Slide 47: Beta multiplier voltage reference
Figure shows the beta multiplier voltage reference. The circuit is the same as previous discussed beta multiplier referenced current source-var.1. The reference voltage is VGS2.
The condition for the temperature compensation is
Applying that
we find that Vref is equal to
and is independent of VDD.

## Slide 48: Temperature characteristic
Figure shows a temperature characteristic of voltage reference circuit. In this chart, the difference between minimum and maximum reference voltage, when the temperature changes from -50oC to 150oC, is 3mV.

## Slide 49: The reference voltage vs. power supply voltage
The figure presents another important characteristic of the voltage references - Vref = f (VDD). In this case the minimum power supply voltage VDDmin is about 1.9V. The slope of the output voltage Vref vs. VDD in the operation region is about 35mV/V.

## Slide 50: Improved band-gap voltage reference
Frequently, in order to minimize the slope of the output voltage Vref vs. power supply voltage VDD (see the previous chart) a cascode current mirror (M3,M7-M4,M6) is used instead of simple current mirror. This approach reduce the effects of the finite output resistance of the MOS transistors.

## Slide 51: Instructions for self-study
The past presentation gives only a first sight on the voltage references. After reading and understanding the presented information you have to study the material from at least one of the following textbooks:
- R. Baker, H. Li, D.Boyce. CMOS Circuit Design, Layout and Simulation, IEEE Press, New York, 2005, ISBN 0-7803-3416-7. Chapter 21.1, 21.3, and 21.4.1, pp.463-484.
- Ph. E. Allen, D. R. Holberg, and Allen. CMOS Analog Circuit Design, Oxford University Press, Inc., 2002. ISBN 0-19-511644-5, Chapter 4.6, pp. 153-159.
- F. Maloberti. Analog design for CMOS VLSI Systems. Kluwer Academic Publishers, 2003, eBook ISBN: 0-306-47952-4, Print ISBN: 0-7923-7550-5, Chapter 4.3 and 4.4, pp.196-215.
The next step in the learning process is to study the examples and complete the experiments, which are presented in Guided exercise 4 and Non-guided exercise 3.
After that you can go on to the next module : CMOS single stage amplifiers